## Slide 1: CPU Organization Course day 2
Alexander Titov
24 December 2014

## Slide 2: Course Roadmap
Day 1
  Pipeline
  Memory Hierarchy (Caches)
Day 2
  Out-of-order execution
  Branch prediction
Day 3
  Real example: Haswell Microarchitecture

## Slide 3: Refresher: Pipeline
Pipeline improves throughput of CPU by overlapping instruction processing
  Max speed is one instruction per clock (IPC = 1; CPI = 1/IPC)
  The real speed is less due to dependencies among instructions (both data and control) and in-order execution
 |  |  | F | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
M | W

## Slide 4: Refresher: Memory Hierarchy
Main memory is large, but too slow
Luckily, there are temporal and spatial locality in our workloads
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 5: Refresher: Caches
Three types of caches
  Fully Associative: no conflict, but slow and complex HW
  Direct MAP: fast and simple HW, but many conflicts
  Multi-Way: something in between (more ways → closer to fully associative)
Example: 32KB, 8 ways, 64B line
Replacement – LRU
Prefetch – predict future accesses
The more levels → the shorter AMAT (but large HW)
64 | 11 |  | 5 | 0
Tag | Set |  | Offset | 
way size = 32KB / 8 = 4KB
# of sets = 4KB / 64B = 64
address
→

## Slide 6: Superscalar: wide pipeline
Pipeline exploits instruction level parallelism (ILP)
Can we do it better?
  Need to double HW structures
  Max speedup is 2 instruction per cycle (IPC = 2)
  The real speedup is less due to dependencies and in-order execution
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
F | Stall
– Yes, execute instructions in parallel

## Slide 7: Is Superscalar Good Enough?
Theoretically can execute multiple instructions in parallel
  Wide pipeline → more performance
But…
  Only independent subsequent instructions can be executed in parallel
  Whereas subsequent instructions are often dependent
  So the utilization of the second pipe is often low
Solution: out-of-order execution
  Execute instructions based on the “data flow” graph, (rather than program order)
  Still need to keep the visibility of in-order execution

## Slide 8: Data Flow Analysis
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
In-order execution
Out-of-order execution
1
3
4
2
5
6
r1
r5
r6
r4
r8
Example:
Data Flow Graph
1
3
4
2
6
5
3
4
6
5
1
2

## Slide 9
Parallel algorithms
Sequential hardware
Sequential code (ISA)
Initially, HW was very simple: sequential execution, one instruction at a time
The sequential code representation was natural and convenient

## Slide 10
Sequential hardware
Then, technology allowed building wide HW, but the code representation has stayed sequential
Decision: extract parallelism back by means of HW
Due to compatibility still need look like sequential HW
Parallel algorithms
Sequential code (ISA)
Sophisticated
parallel
hardware
Visibility of
sequential HW

## Slide 11: Why Is Order Important?
Many mechanisms rely on original program order
  Precise exceptions: nothing after instruction caused an exception can be executed
(1) r3  r1 + r2
  (2) r5  r4 / r3
(3) r2  r7 + r6
  Memory model: inter-thread communication requires that the memory accesses are ordered
  What if they are executed in the following order: (1) → (3) → (2)
  and then (2) leads to exception?
LD A ST B LD B ST A
Load A returns new data, Load B returns old data = NOT ALLOWED
LD A LD B ST B ST A
Both loads return new data = NOT ALLOWED

## Slide 12: Maintaining Arch State
Solution: support two state, speculative and architectural
Update arch state in program order using special buffer called ROB (reorder buffer) or instruction window
  Instructions written and stored in-order
  Instruction leaves ROB (retired) and update arch state only if it is the oldest one and has been executed
Retirement
Instruction window
Out-of-order execution
Fetch & Decode
Sequential code
Visibility of
sequential execution
Out-of-order
In-order
Legend:
Speculative state
Architectural state

## Slide 13: Dependency Check
For each source check its previous producer
Fetch
Retire
HW instruction window (ROB)
Ready, but not executed
Executes
Legend:
Not ready
?
r3  r1 + r2
r1  …
4
7
1
3
0
5
6
2
8
10
9
11
12
13
14
15
r1  …
r2  …
ready
not ready
.., #15
Src1:
Src2:
Consumers:
  If both sources are ready then instruction is ready
  If a source is not ready, write the instr# into the consumer list of producer
When an instruction becomes ready, send a signal to all consumers that their sources become ready too
For loads need also to check addresses of all previous stores

## Slide 14: How Large Is Window Needed?
In short, the large window → the better
  Find more independent instructions
  Hide longer latencies (e.g., cache misses, long operations)
Example
  The modern CPU has a window of 200
  If we want execute 4 instruction per cycle, then we can hide latency of 50 cycles
  It is enough to hide L1 and L2 misses, but not L3 miss
But, there are limitation to find independent instructions in a large window:
  branches and false dependencies

## Slide 15: Limitation: False Dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
Out-of-order execution
Example:
1
3
4
2
5
6
r1
r5
r6
r4
r8
Data Flow Graph
4
3
6
5
1
2
r1
r1
r1
False Dependencies:
Write-After-Write: (1) → (3)
Write-After-Read: (2) → (3)
Significantly decrease performance

## Slide 16: Register Renaming
Redo register allocation that was done by compiler
Eliminate all false dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r1  r5 + 1
(4) r6  r6 – r3
(5) r4  load [ r1 + r6 ]
(6) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15

## Slide 17: Limitation: Branches
How to fill a large window from a single sequential instruction stream in presence of branches?
Fetch
Retire
Branch with unknown condition
All subsequent instructions are fetch according to prediction
…
Speculatively fetched instructions can be executed too
Verify the branch prediction
If prediction was wrong, all the subsequent instructions are deleted
deleted
How harmful are branches?
  In average, each 5th instruction is a branch
  If follow one branch path randomly, then accuracy is 50%
  The probability that 100th instruction in the window will not be removed is (50%)^20 = 0.0001%
Need significantly increase accuracy!

## Slide 18: Dynamic Branch Prediction
Dynamic branch prediction approach:
  As soon as branch is fetched (at IF stage) change the PC to the predicted path
  Switch to the right path after the branch execution if the prediction was wrong
It required complex hardware at IF stage that will predicts:
  Is it a branch
  Branch taken or not
  Taken branch target
Structure performs such function is called BPU

## Slide 19: How To Predict Branch Outcome?
Why four states?
  Bimodal predictor make only one mistake on a loop back branch (on the loop exit)
Advantages:
  Small – only 2 bits per branch
  Predicts well branches with stable behaviour
Disadvantages
  Cannot predict well branches which often change their outcome:
    e.g. T, NT, T, NT, T, NT, T, NT, T, …
A saturating counter or bimodal predictor is a state machine with four states:

## Slide 20: Using History Patterns
1 0 0 1 0 0 1 0 0
0 0 0 0 0 1 0 0 0
past
future
present
History buffer
weakly
NT
strongly
NT
strongly
T
weakly
T
00
weakly
NT
strongly
NT
strongly
T
weakly
T
01
weakly
NT
strongly
NT
strongly
T
weakly
T
10
weakly
NT
strongly
NT
strongly
T
weakly
T
11
Prediction:
TRUE
Result:
FALSE
Pattern history table
Branch sequence:
Remember not just most often outcome, but most often outcome after certain history patterns

## Slide 21: Local Predictor
Local branch predictor has a separate history buffer and pattern table for each branch
Large HW → hard to implement local predictor with large history
History
Prediction
Patterns
PC

## Slide 22: Global Predictor
Global predictor have common history and pattern table for all branches
Can have very large history
  if (a == 3)
  {
  …
  }
  …
  if (a > 6)
  {
  …
  }
Can see correlation among different branches
The real branch predictor is a combination of different local, global and more sophisticated predictors

## Slide 23: Summary
Advantages of OOO Execution
  Help to exploit Instruction Level Parallelism (ILP)
  Help to hide latencies (e.g., cache miss, divide)
  Superior/complementary to the compiler
Complex HW
  Requires reconstruction of original order
  Complex dependency check logic
  Register renaming
  Branch prediction and Speculative Execution

## Slide 24: Q & A