## Slide 1: CPU Organization Course
Alexander Titov
23 December 2014

## Slide 2: Introduction
Who am I?
  Hardware Architect
  7 years in hardware industry (mostly RnD)
  4 years of teaching experience
Why are we here?
  To better understand how microprocessor (CPU) works

## Slide 3
ONE DOES NOT SIMPLY
STUDY MICROPROCESSORS

## Slide 4: Today’s Goal
Processor Microarchitecture for SW engineers
Try to hit the tip of the “iceberg”
Explain the main concepts only
Not enough to develop your own microprocessor…
But, allow better understanding behavior of your programs

## Slide 5: Course Roadmap
Day 1
  Pipeline
  Memory Hierarchy (Caches)
Day 2
  Out-of-order execution
  Branch prediction
Day 3
  Real example: Haswell Microarchitecture

## Slide 6: Layers of Abstraction
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Interface between HW and SW

## Slide 7: Basic CPU Actions
Fetch instruction by PC from memory
Decode it and read its operands from registers
Perform calculation
Read/write memory
Write the result into the registers and update PC
F
D
E
M
W
4ns
8ns
time

## Slide 8: Non-pipelined Processing
instr 1
instr 2
F
D
E
M
W
instr 0
F
D
E
M
Instructions are processed sequentially, one per cycle
How to speedup?
    SW:
    HW:
F
D
E
M
W
F
D
E
M
Sync signal
(clocks)
instr 0
instr 1
instr 2
instructions
time
4ns
8ns
12ns
16ns
F
D
E
M
W
    decrease the number of instructions
    decrease the time to process one instruction
    or overlap their processing, i.e. make pipeline

## Slide 9: Pipeline
wait
F
D
E
M
W
wait
Processing is split into several steps called “stages”
  Each stage takes one clock cycle
  The clock cycle is determined by the longest stage
Instructions are overlapped
  A new instruction occupies a stage as soon as the previous one leaves it
wait
F
D
E
wait
D
F
W
wait
M
W
wait
Sync signal
(clocks)
F
M
E
wait
D
W
wait
M
E
time
4ns
8ns
12ns
16ns
instr 0
instructions
instr 1
instr 2

## Slide 10: Pipeline vs. non-pipeline
wait
F
D
E
wait
D
F
W
wait
M
W
wait
Sync signal
(clocks)
F
E
wait
D
M
W
wait
M
E
time
4ns
8ns
12ns
instr 0
instr 1
instr 2
instructions
instr 1
F
D
E
M
W
Sync signal
(clocks)
instr 0
instr 1
instr 2
instructions
time
4ns
8ns
12ns
16ns
F
D
E
M
W
F
D
E
M
W
Non-Pipelined
pipeline fill
steady state
8 ns
8 ns
2 ns
2 ns
Pipeline improves throughput, not latency
Effective time to process instruction is one clock
  Clock length is defined by the longest stage
Pipelined

## Slide 11: Pipeline Limitations
 |  |  | F | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
Max speed of the pipeline is one instruction per clock
It is rare achievable due to dependencies among instructions (either data or control) and in-order processing
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
M | W

## Slide 12: Memory Hierarchy

## Slide 13: Motivation for Memory Hierarchy
CPU
DRAM
60% per year
(Doubles every 1.5 year)
9% per year
(Doubles every 10 year)
Performance gap

## Slide 14: Memory Tradeoffs
Large memories are slow
Small memories are fast, but expensive and consume high power
Goal: give the processor a feeling that it has a memory which is fast, large, consumes low power and cheap
Solution: a Hierarchy of memories
Speed:
Capacity (size):
Cost:
Power:
Fastest
Smallest
Highest
Highest
Slowest
Biggest
Lowest
Lowest
L1
Cache
CPU
L2
Cache
L3
Cache
Memory
(DRAM)

## Slide 15: Why Is It Works?
Temporal Locality (Locality in Time):
  If an item is accessed, it will tend to be accessed again soon
  Example: code and variables in loops
→ Keep recently accessed data closer to the processor
Spatial Locality (Locality in Space):
  If an item is accessed, nearby items tend to be accessed soon
  Example: scanning an array
→ Move contiguous blocks closer to the processor
Locality + smaller HW is faster memory → hierarchy

## Slide 16: Cache: Main Idea
The cache holds a small part of the entire memory
  Need to map parts of the memory into the cache
Main memory is virtually partitioned into lines
  Typical block size is 32 to 64 bytes
  Blocks are aligned
Memory
Cache
#line
#line
The cache holds data by lines
  Only a subset of the blocks is mapped to the cache at a given time
Address of lines is used as a key
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
91 | 
4 | 
5 | 

## Slide 17: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
2 | 
91 | 
5 | 
Memory
Cache
#line
#line
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
4?
4
hit
CPU

## Slide 18: Cache Lookup
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
93?
4
miss
2
93
93?
CPU
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
  The requested line is not in the cache
  Need to fetch it from the main memory (slow) and fill the cache
  May need to evict another line from the cache to free space for the new one

## Slide 19: Fully Associative Cache
data
Line may be mapped to any cache entry
  Lookup line in all entries
Address is partitioned to
  Offset within a line (byte#)
  Line # (so-called tag)
Each cache entry has a tag
  All tags are compared to the line# in parallel
  If one of the tags matches the line#, we have a hit
63
0
…
hit/miss
=
=
=
…
…
Tag
Array
Data
Array
64 | 5 | 0
Tag = line# | Offset | 
Address
0 | 
1 | 
… | 
511 | 

## Slide 20: Direct Map Cache
Line is mapped to the fixed entry only
  Lookup line in one entry
Address is partitioned to
  Offset within a line (byte #)
  Set (fixed cache entry #)
  Tag (works as a key)
Conflicts are possible
  If several lines are mapped to the same entry, only one can reside in the cache
data
0 |  |  | 
1 |  |  | 
… |  |  | 
511 |  |  | 
63
0
Tag Array
Data
Array
Address
64 | 14 |  | 5 | 0
Tag | Set |  | Offset | 
…
hit/miss
=
set#

## Slide 21: Direct Map Memory Layout
tag#
Memory is virtually partitioned
  into lines
    line size = 2 ^ offset_size
  lines grouped into slices
    # of lines in slices = 2 ^ set_size
    slice size = # of lines in slice * line_size = cache size
  slice # = tag value
  line # inside a slice = set value
…
cache size
cache size
cache size
cache size
Memory Space
set#
set#
set#
set#
Mapped to the same set
Address
 | Offset
 | Set | Offset
Tag | Set | Offset
0
64
Disadvantage is line evictions due to set conflicts

## Slide 22: 2-Way Set Associative Cache
Conflicts are harmful → multi-ways cache is a solution
Each set holds two entries (way 0 and way 1)
  Each line can be mapped into one of two entries in the appropriate set
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #1
set#
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #0
set#

## Slide 23: Multi-way Memory Layout
Memory is virtually partitioned almost the same as in direct map cache
  The only difference is slice size
    slice size = cache size / # of ways
Compared to direct map cache
  Decrease slice size → increase # of slices → increase # of lines mapped to the same set
  But in each set we can have multiple lines (= # of ways) at a given time
…
way size
Memory Space
set#
Mapped to the same set

## Slide 24: 2-Way Set Associative Cache
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 | 
1 | 
… | 
255 | 
63
0
way #0
way #0
set#
hit/miss
=
0 | 
1 | 
… | 
255 | 
set#
way #1
=
63
0
way #1
Tag Array
Data Array
MUX
data

## Slide 25: Line Replacement Policies
Direct map
  A new block is mapped to a single line in the cache
  Old line is evicted (re-written to memory if needed)
N-way set associative cache
  Choose a victim from all ways in the appropriate set
Replacement algorithms
  FIFO (First In First Out)
  Random
  LRU (Least Recently used)
LRU is the best
  but not that much better even than random

## Slide 26: Cache Performance
Terms:
  Miss Rate = Misses / total CPU request
  Hit Rate = Hits / total CPU request = 1 – Miss Rate
Cache goal – decrease memory access time
  AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
Example:
  HitRate ≈ 0.9, HitTime ≈ 4 clk, MissRate ≈ 0.1, MissPenalty ≈ 200 clk, then
  AMAT = 0.9 * 4 + 0.1 * 200 = 23.6 clk
  AMAT w/o cache = 200 clk
  About 10x improve!

## Slide 27: 2-level Cache Performance
Cache L1:
  AMAT = HitTimeL1 + MissRateL1 * MissPenaltyL1
Now, cache L1 accesses not memory, but cache l2
  MissPenaltyL1 = HitTimeL2 + MissRateL2 * MissPenaltyL2
Example

## Slide 28: Prefetching
Prefetching – predict future memory accesses
  Instruction Prefetching
    On a cache miss, prefetch sequential cache line
    Branch predictor run ahead and can trigger prefetching
  Data Prefetching
    Next sequential: on a cache miss, prefetch sequential cache line
    Stride: remember the repetitive step of a load and prefetch data in advance
    General pattern: even if there is no fixed stride can understand general direction and prefetch along it
  Software Prefetching
    Special prefetching instructions that cannot cause faults
Prefetch Limitations
  Prefetching relies on extra memory bandwidth
  Too aggressive / inaccurate prefetching slows down demand fetches

## Slide 29: Code Optimization: Merging Arrays
Merge arrays into an array of compound elements
  Before: two sequential arrays
int val[SIZE];
int key[SIZE];
  After: One array of structures
struct merge {
int val;
int key;
} merged_array[SIZE];
Reduce conflicts between val and key
Improves spatial locality

## Slide 30: Code Optimization: Loop Fusion
Combine loops that have same looping and work with the same memory
  Assume each element is 8 bytes, 32KB cache, 64 B/line
  for (i = 0; i < 10240; i++)
  a[i] = 1 / a[i];
  …
  for (i = 0; i < 10240; i++)
  sum = sum + a[i];
  Fuse the loops
  for (i = 0; i < 10240; i++) {
  a[i] = 1 / a[i];
  sum = sum + a[i];
  }
Improves temporal locality

## Slide 31: Code Optimization: Loop Interchange
Change loops nesting to access data in order stored in memory
  Two dimensional array in memory:
x[0][0] x[0][1] … x[0][99] x[1][0] x[1][1] …
  Before:
  for (j = 0; j < 100; j++)
  for (i = 0; i < 5000; i++)
  x[i][j] = 2 * x[i][j];
  Improves spatial locality
  Sequential accesses instead of striding through memory every 100 words
  for (j = 0; j < 100; j++)
  After:
  for (i = 0; i < 5000; i++)
x[i][j] = 2 * x[i][j];
  for (i = 0; i < 5000; i++)
  for (j = 0; j < 100; j++)
  x[i][j] = 2 * x[i][j];

## Slide 32: Q & A