## Slide 1: Know Your Hardware: CPU Memory Hierarchy
Alexander Titov

## Slide 2: About me
Alexander Titov
  CPU Hardware Architect
  10 years of C++ experience (CPU simulation)
  Teaching Computer Architecture and Design
alexander.titov@atitov.com
alexander-titov-cpu

## Slide 3: How CPU Works?
Outside World
Outside Memory
CPU

## Slide 4: How CPU Works?
Read instruction
Decode it
Read inputs
Execute instruction
Write result
Read next instruction
Decode it
Read inputs
CPU
Outside Memory
Simplified CPU actions:
what to do?
010100…0101
a[0] = b[0] + 1
?
2
a[0] =
3
from MEM
from MEM
to MEM
what next?
Conclusion: CPU works a lot with Outside Memory

## Slide 5: Is Outside Memory Fast?
CPU
Outside Memory
CPU

## Slide 6: Is Outside Memory Fast?
Outside Memory
CPU
– No
~0.5 ns
4x
~100 ns
Memory is very slow.
CPU would wait 99% of the time for Memory response.

## Slide 7: Cache Hierarchy
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
Cache
3rd
level
Cache
2nd
level
Cache
1st level

## Slide 8: Cache Hierarchy In Action
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
miss
miss
miss

## Slide 9: Cache Hierarchy In Action
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
hit
Locality principle:
the same data is requested several times in a short period of time

## Slide 10: Experiment: Defining Cache Hierarchy
intuition
Intel(R) Xeon(R) Gold 6130 CPU, TDP 2.10GHz, Turbo 3.77Ghz
32 KB
1 MB
22 MB
L1 Cache
32 KB
L2 Cache
1MB
L3 Cache
22MB
Outside
Memory
430 GB/s
128 B/cycle
170 GB/s
50 B/cycle
25 GB/s
7 B/cycle
13 GB/s
3 B/cycle

## Slide 11: Performance Optimizations
Rule #1:
  Use tools: google benchmark, perf, Intel VTune Amplifier, etc.
Rule #2: Do educated decisions
Rule #3: Do not reinvent bicycle
  For many tasks there are highly optimized libraries (e.g., Intel MKL)
Rule #4: Optimize in the following order
  General algorithm (e.g., O(NlogN) vs. O(N^2))
  Memory allocation, copy vs. move, etc.
  Data structures organization in memory and access patterns
  Branches, code footprint
  …
Measure it!

## Slide 12: Tip: Divide and Conquer
Split large workload in parts that fit in the cache
→ improve locality
cache size
Large workload
Split workload

## Slide 13: Tip: Divide and Conquer
Split large workload in parts that fit in the cache
30x
speedup
Example:
→ 4096 parts x (16 KB x 1000 times)
64 MB x 1000 times
→ improve locality
cache size
Large workload
Split workload

## Slide 14: Tip: Split Warm and Cold Data
All data transfers are performed in aligned chunks of 64 B (line)
  Even if 1B is requested by instruction, the whole 64B chunk is read
If the rest of the line is not used, it occupies space and BW in vain
Extract fields that are accessed more often (warm) into a separate object

## Slide 15: Tip: Split Warm and Cold Data
0
64
128
struct Mixed {
int warm;
int cold[15];
};
Mixed mixed_array[N];
Extract fields that are accessed more often (warm) into a separate object
struct Warm {
int warm;
};
Warm warm_array[N];
Cold cold_array[N];
struct Cold {
int cold[15];
};
6% efficiency
100% efficiency
Decrease occupied cache space and memory bandwidth by 16x times!
0
64
128

## Slide 16: Tip: Dense Data Packing
By default, C++ has sparse data packing
  Each field is aligned by its size (to prevent line splits)
struct Sparse {
bool b0;
int i;
bool b1;
double d;
};
// 1B
// 4B
// 1B
// 8B
sizeof(Sparse) ==
?
struct _Sparse {
bool b0;
uint8_t padding0[3];
int i;
bool b1;
uint8_t padding0[7];
double d;
};
b0
i
b1
d
#pragma pack(push)
#pragma pack(1)
struct Dense {
bool b0;
int i;
bool b1;
double d;
};
#pragma pack(pop)
sizeof(Dense) ==
struct LessSparse {
bool b0;
bool b1;
int i;
double d;
};
sizeof(LessSparse) ==
b0
i
b1
d
b0
i
b1
d
16
14
24

## Slide 17: Pitfall: Split Atomic
Dense packing can be dangerous. E.g., lead to split line atomics.
#pragma pack(push)
#pragma pack(1)
struct alignas(64) SplitAtomic
{
uint8_t padding[63];
atomic<uint64_t> a;
};
#pragma pack(pop)
struct alignas(64) Atomic
{
uint8_t padding[63];
atomic<uint64_t> a;
};
vs.
A split line atomic is ~300x slower that an usual atomic!
0
64
128
padding
a
atomic is in two lines
0
64
128
padding
a

## Slide 18: Pitfall: False Line Sharing
Shared L3 Cache
Core
Core
Core
Core
System Agent
&
Memory Controller
want to write
snoop
snoop
snoop
snoop
Do not place independent data written by multiple threads into one line!
  If data is only read → OK
// each thread repeatedly writes
// only its own element
int thread_results[4];
Example:
Core must “own” a whole line to be able to write it
  The copies in the other Cores are removed
Each write miss L1 and L2 caches!
If the data were in different lines, it would be L1 hits
0
64

## Slide 19: What Next?
Docs:
  Intel Architectures Optimization Reference Manual
Courses:
  High-Performance Computing and Concurrency by Fedor G. Pikus
Tools:
  Google Benchmark
  godbolt.org / quick-bench.com
  Intel VTune Amplifier

## Slide 20: Many thanks!
Questions welcome :)
alexander.titov@atitov.com
Alexander Titov
alexander-titov-cpu