## Slide 1: Know Your Hardware: CPU Memory Hierarchy
Alexander Titov

## Slide 2: About me
Alexander Titov
  CPU Hardware Architect
  10 years of C++ experience (CPU simulation)
  Teaching Computer Architecture and Design
alexander.titov@atitov.com
alexander-titov-cpu

## Slide 3: How CPU Works?
Outside World
Outside Memory
CPU

## Slide 4: How CPU Works?
Read instruction
Decode it
Read inputs
Execute instruction
Write result
Read next instruction
Decode it
Read inputs
CPU
Outside Memory
Simplified CPU actions:
what to do?
010100…0101
a[0] = b[0] + 1
?
2
a[0] =
3
from MEM
from MEM
to MEM
what next?
Conclusion: CPU works a lot with Outside Memory

## Slide 5: Is Outside Memory Fast?
CPU
Outside Memory
CPU

## Slide 6: Is Outside Memory Fast?
Outside Memory
CPU
– No
~0.5 ns
4x
~100 ns
Memory is very slow.
CPU would wait 99% of the time for Memory response.

## Slide 7: Cache Hierarchy
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
Cache
3rd
level
Cache
2nd
level
Cache
1st level

## Slide 8: Cache Hierarchy In Action
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
miss
miss
miss

## Slide 9: Cache Hierarchy In Action
Outside Memory
CPU
10 GB – 1 TB
10 – 30 MB
256 KB – 1 MB
32 KB
~0.5 ns
~100 ns
~3 ns
~10 ns
~30 ns
hit
Locality principle:
the same data is requested several times in a short period of time

## Slide 10: Experiment: Defining Cache Hierarchy
intuition
Intel(R) Xeon(R) Gold 6130 CPU, TDP 2.10GHz, Turbo 3.77Ghz
32 KB
1 MB
22 MB
L1 Cache
32 KB
L2 Cache
1MB
L3 Cache
22MB
Outside
Memory
430 GB/s
128 B/cycle
170 GB/s
50 B/cycle
25 GB/s
7 B/cycle
13 GB/s
3 B/cycle

## Slide 11: Divide and Conquer
Split large workload in parts that fit in the cache
→ improve locality
cache size
Large workload
Split workload

## Slide 12: Divide and Conquer
Split large workload in parts that fit in the cache
30x
speedup
Example:
→ 4096 parts x (16 KB x 1000 times)
64 MB x 1000 times
→ improve locality
cache size
Large workload
Split workload

## Slide 13: What is inside CPU?

## Slide 14: Many thanks!
Questions welcome :)
alexander.titov@atitov.com
Alexander Titov
alexander-titov-cpu