## Slide 1: GPGPU: what it is and why you should care
Alexander Titov

## Slide 2: About me
Alexander Titov
  Hardware Architect
  11 years of C++ experience (HW simulation)
  Teaching Computer Architecture and Design
alexander.titov@atitov.com
alexander-titov-cpu

## Slide 3: Preface
GPGPU is performing General-Purpose computation on Graphics Processing Units (GPU) instead of CPU
Goal is to understand the basics of GPGPU that are common for all the HW vendors and for all the SW APIs
This talk is not…
  a proper intro to CUDA, OpenCL, SYCL or any other framework
  a discussion on what HW vendor is better, what API is better, etc.
  able to make you a good GPGPU programmer

## Slide 4: GPGPU Myths (?)
GPU is killing CPU
GPU will make your applications 1000x faster
GPU HW is “magic” and it is very different from CPU HW
GPGPU API (e.g., CUDA) is “magic”. It is much easier to write high-performance code for GPU than for CPU

## Slide 5: Why GPGPU?
Core i5-7400T, Kaby Lake, Jan 2017
GPU is already everywhere
  Desktops, laptops, mobile…
  not servers (yet)
  GPU is not a second-class citizen
  GPU area ≥ CPU area
Graphics
(GPU)
Core 0
Core 1
Core 2
Core 3
General Purpose
(CPU)
GPU dramatically accelerates some general-purpose applications compared to CPU
dramatically
some
Gen9 GT2 <- the smallest GPU configuration

## Slide 6: CPU Evolution
A
R
F/D
In Order
Fetch and Decode
Registers
ALU
Extremely simple: one instruction at a cycle, everything is in order
No parallelism

## Slide 7: CPU Evolution
A
R
F/D
In Order
In Order
R
F/D
A
SIMD (DLP)
Single-Instruction-Multiple-Data (SIMD) operations to leverage Data Level Parallelism (DLP)
B[0] = add A[0], 1
B[1] = add A[1], 1
B[2] = add A[2], 1
B[3] = add A[3], 1
B[0:3] = vadd A[0:3], 1
  Example of a SIMD operation:
SIMD registers
SIMD operations

## Slide 8: CPU Evolution
R
F/D
A1
A0
A
R
F/D
In Order
In Order
In Order
R
F/D
A
SuperScalar (ILP)
SIMD (DLP)
SIMD (DLP)
SuperScalar approach: if two (or more) consecutive instructions are independent, execute them in parallel
A very limited solution to exploit Instruction Level Parallelism (ILP)
additional ALU

## Slide 9: CPU Evolution
R
F/D
A1
A0
R
F/D
A1
A0
$
A
R
F/D
In Order
In Order
In Order
In Order
R
F/D
A
SuperScalar (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
SIMD (DLP)
SIMD (DLP)
Memory access latency is becoming a problem
Adding HW Caches and prefetch to mitigate it
HW Cache

## Slide 10: CPU Evolution
R
F/D
A1
A0
R
F/D
A1
A0
$
A
R
F/D
In Order
In Order
In Order
In Order
R
F/D
A
SuperScalar (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
SIMD (DLP)
SIMD (DLP)
Use sophisticated HW to extract more ILP by executing independent instruction out-of-order
R
F/D
A1
A0
L1
A2
L2
OOO
BP
Out-of-order (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
Out-of-order scheduler
Branch prediction

## Slide 11: CPU Evolution
R
F/D
A1
A0
R
F/D
A1
A0
$
A
R
F/D
In Order
In Order
In Order
In Order
R
F/D
A
SuperScalar (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
SIMD (DLP)
SIMD (DLP)
Adding another thread(s) to execute while the first thread is stalled
R
F/D
A1
A0
L1
A2
L2
OOO
BP
Out-of-order (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
Out-of-order (ILP)
Multi-Thread (TLP)
SuperScalar (ILP)
Caches
SIMD (DLP)
A1
A0
L1
A2
L2
BP
F/D
OOO
R
t0
t1
single-thread
1x
1x
multi-thread
1.5x
1.5x
throughput is higher,
but each thread is slower

## Slide 12: CPU Evolution
R
F/D
A1
A0
R
F/D
A1
A0
$
A
R
F/D
In Order
In Order
In Order
In Order
R
F/D
A
SuperScalar (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
SIMD (DLP)
SIMD (DLP)
Occupy available area by many cores
R
F/D
A1
A0
L1
A2
L2
OOO
BP
Out-of-order (ILP)
SuperScalar (ILP)
Caches
SIMD (DLP)
Out-of-order (ILP)
Multi-Thread (TLP)
SuperScalar (ILP)
Caches
SIMD (DLP)
A1
A0
L1
A2
L2
BP
F/D
OOO
R
t0
t1
L3
…
Out-of-order (ILP)
Multi-Thread-Core (TLP)
SuperScalar (ILP)
Caches
SIMD (DLP)
A1
A0
L1
A2
L2
BP
F/D
OOO
R
t0
t1
A1
A0
L1
A2
L2
BP
F/D
OOO
R
tN-1
tN

## Slide 13: CPU Evolution: Performance Trends
Data up to 2010 collected by M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, and C. Batten. Data for 2010-2017 by K. Rupp
101
102
103
104
105
106
107
108
1
Majority of applications cannot utilize more than 4-8 cores
About 5-10% of applications are well scaled
→ need many simple cores
→ need a few large cores
Cannot optimize CPUs for 5-10% applications
Need to develop another device?
→ No, it is already available
Myth: GPU is killing CPU

## Slide 14: GPU Evolution (toward GPGPU)
Initially, GPU was designed strictly for rendering 2D and 3D
Graphic pipeline was fixed and could not be programmed
Graphic Pipeline
Non-Programmable

## Slide 15: GPU Evolution (toward GPGPU)
Impossible to create special HW for all the demanded rendering functionality → programmability is needed
What is a typical rendering task?
  the same actions on multiple independent elements (e.g., turn pixels color to gray)
  processing time of a single element is not important, only total time matter
→ it is SIMD!
R
F/D
A
In Order
SIMD (DLP)
→ it is throughput!
R
F/D
A
t0
t1
tN
tN-1
…
In Order
SIMD (DLP)
High Multi-Thread (TLP)
Many threads to hide latencies (8-16 in practice)
Large register file to keep registers of all the thread

## Slide 16: GPU Evolution (toward GPGPU)
Impossible to create special HW for all the demanded rendering functionality → programmability is needed
What is a typical rendering task?
  the same actions on multiple independent elements (e.g., turn pixels color to gray)
  processing time of a single element is not important, only total time matter
Graphic Pipeline
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Programmable
(Shaders)
→ it is SIMD!
→ it is throughput!
R
F/D
A
R
F/D
A
t0
t1
tN
tN-1
…
In Order
SIMD (DLP)
In Order
SIMD (DLP)
High Multi-Thread (TLP)
t1
t0
t2
…
tK
tK+1
tK+2
…
EU0
GPU HW is “magic” and it is very different from CPU HW

## Slide 17: CPU HW vs GPU HW
Similar HW techniques, just optimized for different purposes
CPU
GPU
good for throughput only
large ILP
no ILP
large DLP (SIMD)
large DLP (SIMD)
medium TLP
extreme TLP
good for everything
the best for single-thread
  Myth: GPU HW is “magic” and it is very different from CPU HW

## Slide 18: How Fast GPU vs. CPU?
There are a lot of misunderstanding and black marketing:
What is a core on GPU?
Are CPU and GPU cores are comparable?

## Slide 19: How Fast GPU vs. CPU?
There are a lot of misunderstanding and black marketing:
Need to compare with throughput applications on many cores

## Slide 20: How Fast GPU vs. CPU?
 | 2080 Ti (Turing), 2017Y | Xeon 8168 (Skylake), 2017Y | GPU / CPU
It is reasonable to say that GPU is up to ~10x faster than CPU (36x for ML)
  Myth: GPU will make your applications 1000x faster
Cores
4352
24
181x
Compute capacity
14 TFLOPS (FP32)
~3 TFLOPS (FP32)
5x
110 TFLOPS (FP16 tensor cores)
36x
Memory BW
616 GB/s
120 GB/s
5x
Area
754 mm2
694 mm2
~1x
Price
1000$
6000x
6x

## Slide 21: GPGPU Programming
There are many GPGPU APIs for C/C++:
  CUDA: many features, easy-to-use, but not open and not portable (only NVIDIA)
  OpenCL: less features, verbose, but open and portable (Intel, AMD, NVIDIA, etc.)
  SYCL: based on OpenCL, easy-to-use, more C++ oriented, but still in development
All APIs are based on the offload model: host (CPU) prepares and controls everything, device (GPU) only execute
Code is divided in the two parts:
  the device code (kernel) written in a subset of C/C++
  the host code in your C/C++ program

## Slide 22: Kernel Code (Open CL)
How to program this crazy mix of vectors and threads?
Big Idea: as it is SIMD, write code for a single data element only
  The kernel compiler forms vectors and create threads on its own
void
mul(const float *a,
const float *b,
float *c,
const int n)
{
for (int i = 0; i < n; i++)
c[i] = a[i] * b[i];
}
Traditional Loop
__kernel void
mul(__global const float *a,
__global const float *b,
__global float *c)
{
int i = get_global_id(0);
c[i] = a[i] * b[i];
}
Data parallel OpenCL
t1
t0
t2
…
tK
tK+1
tK+2
…
EU0

## Slide 23: Kernel Code (Open CL)
Is everything so simple?
Problem: Divergent control flow decreases utilization
__kernel void
foo(__global const float *a,
__global const float *b,
__global float *c)
{
int i = get_global_id(0);
if (i % 2)
c[i] = a[i] * a[i];
else
c[i] = b[i] * b[i];
}
mask = {0, 1, 0, 1, 0, 1, 0, 1} c[0:7] = vmul a[0:7], a[0:7], mask
c[0:7] = vmul b[0:7], b[0:7], !mask
half of elements is calculated, but dropped
→ in toy examples – yes, but not in the real world

## Slide 24: Kernel Code (Open CL)
Is everything so simple?
Problem: Divergent control flow decreases utilization
Problem: Tuning for GPU layout is required
→ in toy examples – yes, but not in the real world
L2
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
L1
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
L1
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
L1
Graphic Pipeline
Compute
Dispatch
Matrix Multiplication Approaches | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
C row per work-item, all global | 61.8 | 9.1
C row per work-item, A row private | 9.6 | 24.9
C row per work-item, A private, B local | 12.3 | 55.4
Block oriented approach using local | 138.0 | 1,801.8
11.5% of peak
21.2% of peak
Hand on OpenCL Workshop, UoB-HPC, 2018
Myth: It is much easier to write high-performance code for GPU than for CPU

## Slide 25: Conclusions
5-10x speedup is good to invest
APIs are mature for production, but still evolve
Entry threshold is medium
Writing high-performance code is as hard as on CPU

## Slide 26: Many thanks!
Questions welcome :)
alexander.titov@atitov.com
Alexander Titov
alexander-titov-cpu