## Slide 1: Know Your Hardware: CPU Memory Hierarchy
Alexander Titov

## Slide 2: About me
Alexander Titov
  CPU Hardware Architect
  10+ years of C++ experience (CPU simulation)
  Teaching Computer Architecture and Design
alexander.titov@atitov.com
alexander-titov-cpu

## Slide 3: Performance Optimizations Rules
Do not do it 
0.
Measure it!
Do educated decisions
Do not reinvent the wheel
Optimize in the following order
  General algorithm (e.g., O(NlogN) vs. O(N^2))
  Memory allocation, copy vs. move, etc.
  Data organization in memory and access patterns
  Code footprint
  Branches
  …
  Data organization in memory and access patterns

## Slide 4: Why Is Memory So Important?
Read instruction from memory
Decode it
Read inputs from memory
Execute instruction
Write result to memory
Read next instruction from memory
Decode it
Read inputs from memory
Simplified steps to execute an instruction:
010100…0101
a[0] = b[0] + 1
?
2
a[0] =
3
what next?
CPU works a lot with Memory

## Slide 5: Is Memory Fast?
Read instruction from memory
Decode it
Read inputs from memory
Execute instruction
Write result to memory
Simplified steps to execute an instruction:
CPU
~0.5 ns

## Slide 6: Is Memory Fast?
Read instruction from memory
Decode it
Read inputs from memory
Execute instruction
Write result to memory
Simplified steps to execute an instruction:
CPU
~0.5 ns

## Slide 7: Is Memory Fast?
Memory
CPU
– No
~0.5 ns
4x
~100 ns
Memory is very slow.
CPU would wait 99% of the time for Memory response.

## Slide 8: Cache Hierarchy in Real Life
3rd level
cache
1st level
cache
2nd level
cache
Factory
Home
Small shop
Large store
Warehouse

## Slide 9: Cache Hierarchy
Memory
CPU
3rd level
cache
2nd level
cache
1st level
cache

## Slide 10: Cache Hierarchy In Action
Memory
CPU
miss
miss
miss

## Slide 11: Cache Hierarchy In Action
Memory
CPU
Locality principle:
the same data is requested several times in a short period of time
hit

## Slide 12: Cache Hierarchy
10 GB – 1 TB
Memory
CPU
10 – 30 MB
256 KB – 1 MB
32 KB
3rd level
cache
2nd level
cache
1st level
cache
? GB/s
? GB/s
? GB/s
? GB/s

## Slide 13: Experiment: Defining Cache Hierarchy
Benchmark structure
start
end
N times

## Slide 14: Experiment: Defining Cache Hierarchy
Memory
L3 cache
L2 cache
L1 cache
Benchmark structure

## Slide 15: Experiment: Defining Cache Hierarchy
intuition
Intel(R) Xeon(R) Gold 6242 CPU, TDP 2.80GHz, Turbo 3.90Ghz
32 KB
1 MB
22 MB
L1 Cache
32 KB
L2 Cache
1MB
L3 Cache
22MB
Outside
Memory
400 GB/s
220 GB/s
25 GB/s
16 GB/s
25x
14x
1.5x
1x

## Slide 16: Multi-Core CPU
Memory
CPU
L3
L2
L1

## Slide 17: Multi-Core CPU
Memory
L3
L2
L1
Core 0
L2
Core N
L1
Core N
Core N
…
Shared
Core 0
Core 0
IL1
Core N
IL1
Core N
N times more space and BW than in a single core
?

## Slide 18: Experiment: Single-Core vs. Multi-Core
Intel(R) Xeon(R) Gold 6242 CPU, TDP 2.80GHz, Turbo 3.90Ghz, 16 Cores
multi-thread
(16 threads; the same code,
but different memory; sum BW is shown)
single-thread
~16 x
~16 x
~16 x
95 GB/s vs 16 GB/s
~6 x
Multi-threaded application receives not only N x cache space and BW,
but large Memory BW too

## Slide 19: Tip: Divide and Conquer
Cache
Split large workload in parts that fit in the cache
→ improve locality
N times
N times
N times
N times
N times
20x
speedup
Example:
→ 4096 parts x (16 KB x 1000 times)
64 MB x 1000 times

## Slide 20: Memory line
All data transfers are performed in aligned chunks of 64 B (memory line)
  If the rest of the line is not used, it occupies space and BW in vain
Memory
CPU
N * 64
(N+1) * 64
The better line utilization → the better performance
Control info: address, state, protection, etc.

## Slide 21: Tip: Split Warm and Cold Data
0
64
128
struct Mixed {
int warm;
int cold[15];
};
Mixed mixed_array[N];
Extract fields that are accessed more often (warm) into a separate object
struct Warm {
int warm;
};
Warm warm_array[N];
Cold cold_array[N];
struct Cold {
int cold[15];
};
6% efficiency
100% efficiency
Decrease occupied cache space and memory bandwidth by 16x times!
0
64
128

## Slide 22: Tip: Dense Data Packing
By default, C++ has sparse data packing
  Each field is aligned by its size (to prevent line splits)
struct Sparse {
bool b0;
int i;
bool b1;
double d;
};
// 1B
// 4B
// 1B
// 8B
sizeof(Sparse) ==
?
struct _Sparse {
bool b0;
uint8_t padding0[3];
int i;
bool b1;
uint8_t padding0[7];
double d;
};
b0
i
b1
d
#pragma pack(push)
#pragma pack(1)
struct Dense {
bool b0;
int i;
bool b1;
double d;
};
#pragma pack(pop)
sizeof(Dense) ==
struct LessSparse {
bool b0;
bool b1;
int i;
double d;
};
sizeof(LessSparse) ==
b0
i
b1
d
b0
i
b1
d
16
14
24

## Slide 23: Pitfall: Split Atomic
Dense packing can be dangerous. E.g., lead to split line atomics.
#pragma pack(push)
#pragma pack(1)
struct alignas(64) SplitAtomic
{
uint8_t padding[63];
atomic<uint64_t> a;
};
#pragma pack(pop)
struct alignas(64) Atomic
{
uint8_t padding[63];
atomic<uint64_t> a;
};
vs.
A split line atomic is ~300x slower that an usual atomic!
0
64
128
padding
a
atomic is in two lines
0
64
128
padding
a

## Slide 24: What Next?
Not discussed: virtual memory (TLB), prefetching, coherency, cache conflicts, memory types (UC, WC, etc.), cache inclusion/exclusion, memory ordering, replacement policies, false sharing, thread cross-trashing, …
Courses: MIPT, Princeton, Technion, Berkley CS152/CS61C, UW CSE378, MIT 6.004, CMU 18-447
Books: Computer Organization and Design, Computer Architecture, Modern Processor Design
Docs: Intel Architectures Optimization Reference Manual
Tools: Google Benchmark, godbolt.org / quick-bench.com, Intel VTune Amplifier

## Slide 25: Many thanks!
Questions welcome :)
alexander.titov@atitov.com
Alexander Titov
alexander-titov-cpu

## Slide 26: Pitfall: False Line Sharing
Shared L3 Cache
Core
Core
Core
Core
System Agent
&
Memory Controller
want to write
snoop
snoop
snoop
snoop
Do not place independent data written by multiple threads into one line!
  If data is only read → OK
// each thread repeatedly writes
// only its own element
int thread_results[4];
Example:
Core must “own” a whole line to be able to write it
  The copies in the other Cores are removed
Each write miss L1 and L2 caches!
If the data were in different lines, it would be L1 hits
0
64
L1
L2
L1
L2
L1
L2
L1
L2

## Slide 27: Experiment: Sparse Access Pattern
What if requests are not adjacent?
benchmark 1
64B
64B
step
benchmark 2
128B
step
benchmark 3
196B
step
…

## Slide 28: Experiment: Sparse Access Pattern
Workload size is the same for all the tests – 1 MB
Intel(R) Xeon(R) Gold 6242 CPU, TDP 2.80GHz, Turbo 3.90Ghz

## Slide 29: Cache Structure
Cache
Cache block of 64B
64B
Memory

## Slide 30: Cache Structure
Cache
ways
sets
Memory

## Slide 31: What is going on with sparse patterns?
Cache
ways
sets
Memory
128B
step

## Slide 32: Cache Hierarchy
10 GB – 1 TB
Outside Memory
10 – 30 MB
256 KB – 1 MB
32 KB
~100 ns
~3 ns
~10 ns
~30 ns
Cache
3rd
level
Cache
2nd
level
Cache
1st level
~0.5 ns
CPU

## Slide 33: Cache Hierarchy in Multi-Core CPU
10 GB – 1 TB
Outside Memory
~100 ns
Cache
3rd
level
Cache
2nd
level
Cache
1st level
Cache
2nd
level
Cache
1st level
…
CPU
0
CPU
N