## Slide 1: CPU Organization Course day 3
Alexander Titov
26 December 2014

## Slide 2: Course Roadmap
Day 1
  Pipeline
  Memory Hierarchy (Caches)
Day 2
  Out-of-order execution
  Branch prediction
Day 3
  Real example: Haswell Microarchitecture

## Slide 3: Refresher: OOO Exe
Superscalar – wide pipeline (4-5 in modern CPU)
Out-of-order – execute according real dependencies (“data flow”) rather than program order
Advantages:
  Extract parallelism from the sequential instr stream
  Hide latencies (e.g., cache misses)
Need to maintain visibility of in-order execution
  Precise exceptions, memory model, etc.

## Slide 4: Refresher: OOO Exe
Two states are supported: speculative and architectural
Instruction window (ROB) keeps all in-flight instructions and allows order reconstructions
The large window the better performance
Limitations:
  False dependencies -> rename registers
  Branches -> accurate dynamic prediction

## Slide 5: Intel Processor Roadmap
Tick-Tock model
  A new microarchitecture (Tock) is followed by process compaction (Tick)
from wikipedia.org

## Slide 6: Haswell FloorPlan
22nm process
1.4 Billion transistors
Die size: 160 mm2
Shared L3 Cache
Core
Core
Core
Core
Processor
Graphics
System Agent
&
Memory Controller

## Slide 7: Haswell Family FloorPlans

## Slide 8
Front End
OOO
EXE
MEM
FE
MEM
EXE
OOO
Block Diagram
FloorPlan Map

## Slide 9: Front End
Instruction Fetch and Decode
  32KB 8-way ICache
  4 Decoders, up to 4 instructions / cycle
  CISC to RISC transformation
  Decode Pipeline supports 16 bytes per cycle
  Cache of Decoded Uops

## Slide 10: Front End: Instruction Decode
Four decoding units decode instruction into uops
  The first can decode all instructions up to four uops in size
  The remaining 3 decoders handle common single uop instructions
Uops emitted by the decoders are directed to the Decode Queue and to the Decoded Uop Cache
Instructions with >4 uops generate their uops from the MSROM
  The MSROM bandwidth is four μops per cycle

## Slide 11: Front End: Decoded Uop Cache
Skips fetch and decode for the cached uops
  Reduces latency on branch mispredictions
  Increases uop delivery bandwidth to the OOO engine
  Reduces front end power consumption
The UC is virtually addressed
  Flushed on a context switch
The UC is an accelerator of the legacy decode pipeline
  Caches the uops coming out of the instruction decoder
  Next time uops are taken from the UC
  The UC holds up to 1536 uops
  Average hit rate of 80% of the uops

## Slide 12: Front End: Loop Stream Detector
LSD detects small loops that fit in the Decode Queue
  The loop streams from the uop queue, with no more fetching, decoding, or reading μops from any of the caches
  Works until a branch misprediction
The loops with the following attributes qualify for LSD replay
  Up to 56 uops
  All uops are also resident in the UC
  No more than eight taken branches
  No CALL or RET
  No mismatched stack operations (e.g., more PUSH than POP)

## Slide 13: Front End: Macro-Fusion
The first instruction of a macro-fused pair modifies flags
  CMP, TEST, ADD, SUB, AND, INC, DEC
The 2nd inst. of a macro-fusible pair is a conditional branch
  For each first instruction, some branches can fuse with it
These pairs are common in many types of applications
Merge two instructions into a single μop
  Increased decode, rename and retire bandwidth
  Power savings from representing more work in fewer bits

## Slide 14: OOO Structures
 | Nehalem | Sandy Bridge | Haswell
Window (BOB) | 128 | 168 | 192
In-flight Loads (LB) | 48 | 64 | 72
In-flight Stores (SB) | 32 | 36 | 42
Scheduler Entries (RS) | 36 | 54 | 60
Integer Registers | Equal to ROB | 160 | 168
FP Registers | Equal to ROB | 144 | 168

## Slide 15: OOO: Renamer
Rename 4 uops / cycle and provide to the OOO engine
  Renames architectural sources and destinations of the uops to micro-architectural sources and destinations
  Allocates resources to the uops, e.g., load or store buffers
  Binds the uop to an appropriate dispatch port
Some uops can execute to completion during rename, effectively costing no execution bandwidth
  Zero idioms (dependency breaking idioms)
  NOP
  VZEROUPPER
  FXCHG
  A subset of register-to-register MOV
The renamer can allocate two branches each cycle

## Slide 16: OOO: Dependency Breaking Idioms
Move elimination
  Moves just update RAT w/o real copy of register value
  Example: eax is renamed to pr10,
  after mov eax->ebx, ebx is also renamed to pr10
Instruction parallelism can be improved by zeroing register content
Zero idiom examples
  XOR REG,REG
  SUB REG,REG
Zero idioms are detected and removed by the renamer
  Have zero execution latency
  They do not consume any execution resource

## Slide 17: EXE

## Slide 18: Core Cache Size/Latency/BW

## Slide 19: ST vs MT
vs
1x area
1x perf
ST
1x width
4x area
1.5x perf
ST
2x width
1x area
1x perf
1x area
1x perf
1x area
1x perf
1x area
1x perf
MT
4x width
1x perf
1x perf
SMT

## Slide 20
EXE
MEM
Block Diagram
FE 0
FE 1
OOO 0
OOO 1

## Slide 21: Q & A