## Slide 1: MIPT-MIPS 2013 Sequential logic. Critical paths.
Pavel Kryukov
02.11.2013

## Slide 2: Layers of Abstraction in Computes Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture
Less about physics, wires and transistors…
More about logical circuits

## Slide 3: Combinational and sequential logic
If the output of a function is completely defined by the current input then the function is called combinational.
Ft = F(xt, yt, zt)
F = F(xt, yt, zt, Ft-1)
combinational
sequential
Combinational logic (scheme) is an implementation of a combinational function.
But how is sequential logic made?

## Slide 4: SR Flip-Flop
set
reset
!Q
Q
S | R | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
no change
resets to 0
sets to 1
forbidden!
x
0
!x
x
1
0

## Slide 5: SR unbalanced situation
0
0
0
0
0
0
1
1
Where will ‘1’ appear first?

## Slide 6: D Flip-Flop
D | E | Q(t) | Q(t+1)
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 1 | 1 | 1
no change
returns D
S
Q
R
!Q
enable
data
How can we use this device?
We can make a memory array!

## Slide 7: Memory array
Memory
…
address (M bits)
…
input data
…
output data
(N bits)
Memory
address
input data
output data
M
N
N
Can store 2M lines of data
Each line is N bits long
So, every line can contain number from 0 to 2N−1
Is used for register file of CPU
Write enable

## Slide 8: Critical paths

## Slide 9: What is a critical path of scheme?
Critical path is the slowest logic path in the circuit
Reliable result of whole logic path can not be ready until critical path is passed by signal

## Slide 10: Example of critical path finding: Multiplexer

## Slide 11: Example of critical path finding: 2-bit adder

## Slide 12: Thank You