## Slide 1: MIPT-MIPS 2013 Sequential logic
Alexander Titov
09.11.2013

## Slide 2: Layers of Abstraction in Computes Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 3: Refresher: Combinational vs. Sequential Circtuis
But, combinational circuits have a significant limitation: they cannot remember any information
If the output of a function is completely defined by the current input then the function is called combinational:
Qt = F(xt, yt, zt, …)
Combinational circuit (scheme) is an implementation of a combinational function
A lot of things can be implemented using combinational circuits
    Just a few examples that we already know: summator, decoder, multiplexer
But, combinational circuits have a significant limitation:

## Slide 4: Refresher: Sequential Circuits
Sequential circuits are able to store information
If the output of a function depends not only on the current input, but on the previous state, then the function is called sequential
Qt = F(xt, yt, zt, …, Qt-1)
F(xt-1, yt-1, zt-1, …, Qt-2))
F(xt-2, yt-2, zt-2, …, Qt-3)))
Qt = F(xt, yt, zt, …, Qt-1)
Sequential circuit is an implementation of a sequential function
Their main advantage is ability to remember the previous state
    Any circuit with memory is a sequential circuits

## Slide 5: Refresher: SR Flip-Flop
S | R | Qt-1 | Qt
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
set
reset
!Q
Q
S
Q
R
!Q
S | R | Qt-1 | Qt
0 | 0 | Q | Q
0 | 1 | Q | 0
1 | 0 | Q | 1
1 | 1 | Q | 0
S
0
1
R
0
1
Q
0
1
!Q
0
1
?
?
But, which signal will be really faster will depend on many factors (e.g., temperature).
The output will be determined by the fastest signal

## Slide 6: Refresher: D Flip-Flop
S
Q
R
!Q
enable
Data
D
e
Q
D | e | Qt-1 | Qt
D | 0 | Q | Q
0 | 1 | Q | 0
1 | 1 | Q | 1
Don’t have prohibited states
Store one bit of information
Can be used as building block for creating static memory arrays

## Slide 7: Single port 2^MxN Memory Array
Memory
Array
address
input data
output data
M
N
N
Write enable

## Slide 8: Single port 4x1 Memory Array
Memory
Array
address
input data
output data
2
1
1
Write enable

## Slide 9: Single port 4x1 Memory Array

## Slide 10: Single port 4x2 Memory Array

## Slide 11: Arithmetic Logic Unit

## Slide 12: MIPS ALU with Register File

## Slide 13: Thank You Q/A