## Slide 1: MIPT-MIPS 2013 Intro to MIPS ISA
Alexander Titov
30.11.2013

## Slide 2: Layers of Abstraction in Computes Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 3: Assembly vs. Machine Language
So far you’ve been using assembly language (mostly x86 MASM in the ASM course of Severov)
  You assign names to operations (e.g., add) and operands (e.g., eax)
  Branches and jumps use labels instead of actual addresses
  Assemblers support many pseudo-instructions (do not really exist in ISA, transformed into the real instructions by an assembler)
Programs must eventually be translated into machine language, a binary format that can be stored in memory and decoded by the CPU
Unlike x86 (CISC) the MIPS (RISC) machine language is designed to be easy to decode
  Each MIPS instruction is the same length, 32 bits
  There are only three different instruction formats (R, I and J), which are very similar to each other

## Slide 4: MIPS: Register-To-Register, Three Address
MIPS is a register-to-register, or load/store, architecture
  The destination and sources must all be registers
  Special instructions, which we’ll see soon, are needed to access main memory
MIPS uses three-address instructions for data manipulation
  Each ALU instruction contains a destination and two sources
  For example, an addition instruction (a = b + c) has the form:
add a, b, c
operands
operation
destination
source 1
source 2

## Slide 5: MIPS Register File
MIPS processors have 32 registers, each of which holds a 32-bit value
  Register addresses are 5 bits long
  The data inputs and outputs are 32-bits wide
More registers might seem better, but there is a limit to the goodness
  The more register the larger decoders, multiplexers, etc. → larger circuits delays
  Instruction length is affected, as need more space to encode register numbers

## Slide 6: MIPS Register Names
MIPS register names begin with a $. There are two naming conventions:
  By number:
      $0 $1 $2 … $31
    By (mostly) two-character names, such as:
      $a0-$a3 $s0-$s7 $t0-$t9 $sp $ra
Number | Name
$0 | $zero
$1 | $at
$2, $3 | $v0, $v1
$4 - $7 | $a0 - $a3
$8 - $15 | $t0 - $t7
$15 - $23 | $s0 - $s7
$24, $25 | $t8, $t9
$26, $27 | $k0, $k1
$28 | $gp
$29 | $sp
$30 | $fp
$31 | $ra
Detailed description of each register can be seen by this link
Why so many different registers?
  Not all of them are general purpose registers (GPR)
  There are a lot of special purposes: procedure mechanism, exception/interrupt handling, etc.
In our project mostly GRPs are used: $t and $s

## Slide 7: R-type Format
Register-to-register (three register operands) arithmetic instructions use the R-type format:
This format includes six different fields:
  op is an operation code that selects a specific action (also defines the format)
  rs and rt are the first and second source registers
  rd is the destination register
  shamt is only used for shift instructions
  func is used together with op to select an arithmetic instruction
Example:
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
000000| 10001 | 10010 | 01000 | 00000 | 100000
opcode
rs
rt
rd
shamt
funct
add
$s1
$s2
$t0
signed

## Slide 8: Immediate Operands
R-type instructions take data from registers. How does it occur there?
  From the memory (on the next foils)
  From immediate
MIPS allows to specify a immediate value (signed constant), for the second source instead of a register, i.e. instead of rt
  For example: addi $t0, $t1, 4 # $t0 = $t1 + 4
rt field is too small to preset real constants
  5 bits → values from [-16; 15]
Cannot use R-type format to encode such instructions → need a new format

## Slide 9: I-type Format for ALU Instructions
ALU instructions with immediate (two register operands) use the I-type format:
For uniformity, op, rs and rt are in the same positions as in the R-type format
This format includes four different fields:
  rs is a source register (first operand)
  rt is a destination register
  imm is a signed value of the second operand
The immediate can range from -32,768 to +32,767
  But that’s not always enough → need to write to a register by halves
op
rs
rt
imm
6 bits
5 bits
5 bits
16 bits

## Slide 10: I-type Format for Loads/Stores
for( int i=0; i < L; i++)
{
int v1 = array[i].v1;
int v2 = array[i].v2;
…
}
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
I-type format is also used for memory operations (load/store) as they are usually have constant memory displacement:
This format includes four different fields:
  rs is a source register, the base of an address for loads and stores
  rt is a source register for stores, but a destination register for loads
  offset is used as an increment to the base to get the address
Examples
lw $t1, 0x0004($t2) # Read 4B into $t1 from Mem[ Reg[ $t2] + 0004]
sw $t1, 0x0004($t2) # Write 4B from $t1 into Mem[ Reg[ $t2] + 0004]

## Slide 11: I-type Format for Branches
I-type format is also used for branches.
The target address is calculated as the end address of the branch (PC+4) plus the displacement encoded in the instruction
This format includes four different fields:
  rs and rt are the first and second source registers
  offset is specified in terms of words instead of bytes:
  target PC = ( PC + 4) + offset << 2
The branch condition is calculated depending on opcode and source values:
  For example, beq write the target address into PC only if its source operands are equal
beq $t1, $t2, L
add $s1, $s0, $0
add $t3, $t1, $t1
L:
add $v1, $v0, $v0
op
rs
rt
offset in words
6 bits
5 bits
5 bits
16 bits

## Slide 12: J-type format
J-type format is used for instructions that do not access any specified register. They are usually unconditional branches (jumps)
Unlike I-type branches, the offset is not added, but change the least bits of PC:
  target PC = ( PC & 0xf0000000 ) | offset << 2
op
offset in words
6 bits
26 bits

## Slide 13: Conclusion
R-type format
I-type format
J-type format
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
op
rs
rt
offset in words
6 bits
5 bits
5 bits
16 bits
op
offset in words
6 bits
26 bits

## Slide 14: Acknowledgements
These slides contain material developed and copyright by:
Luis Ceze (UW), CS378, L1 and L6

## Slide 15: Thank You Q/A