## Slide 1: Memory Hierarchy (part II)
Alexander Titov
21 March 2015

## Slide 2: Refresher: Memory Hierarchy
Main memory is large, but too slow
Luckily, there are temporal and spatial locality in our workloads
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 3: Refresher: Caches
Three types of caches
  Fully Associative: no conflict, but slow and complex HW
  Direct MAP: fast and simple HW, but many conflicts
  Multi-Way: something in between (more ways → closer to fully associative)
Example: 32KB, 8 ways, 64B line
To estimate performance use average access time
    AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
64 | 11 |  | 5 | 0
Tag | Set |  | Offset | 
way size = 32KB / 8 = 4KB
# of sets = 4KB / 64B = 64
address
→

## Slide 4: Three Types of Cache Misses (3-C)
Compulsory misses
  Those that occurs even in a infinite cache
  First access to data
  So-called cold misses
Capacity misses
  Those that occurs in an fully associative cache
  Workset is larger than the cache size
Conflict misses
  Difference between fully associate and direct mapped cache
  The size of the cache is enough, but the problem is in line mapping to sets
Compulsory
Conflict
Capacity
Miss Rate = F(Cache Capacity, Associativity)

## Slide 5: Cache Line Replacement
When miss occurs need to free space in a cache for a new line
Direct mapped cache
  A new line is mapped to a single entry → evict old line from the entry
N-way set associative cache
  Choose a victim from all ways in the appropriate set, but how?
FIFO (First In First Out) replacement
  Easy to implement in HW, but can violate temporal locality
LRU (Least Recently Used) replacement
  Evict the most unused line (was not accessed longer than other)
  Good temporal locality, but complex HW → use simplified pseudo-LRU

## Slide 6: Write Handling
Memory writes (store instructions) also need to update a cache
  If update only memory, the old data can be read from the cache later
There two main approached of write handling
  WriteTrough: always update both memory and cache
  WriteBack: update only cache, update memory at line eviction
Event | WriteTrough | WriteBack
Event | WriteTrough | WriteBack
Write hits cache | Update memory and cache | Update only cache (make line “dirty”)
Write misses cache | Option 1: Upload missing line into cache, update memory and cache Option 2: Update only memory | Upload missing line into cache, update only cache (make the line “dirty)
A line is evicted | Do nothing | If the line is “dirty” write it back into memory

## Slide 7: Small Summary
Where can a block placed?
  One place → direct mapped
  A few places → set associative
  Any place → full associative
What line is replaced on a miss?
  FIFO
  LRU
  Pseudo-LRU
How are writes handled?
  WriteThrough
  WriteBack
How is a block found?
  Indexing → direct mapped
  Limited search → set associative
  Full search → full associative

## Slide 8: Multi-Level Caches
L1 cache: AMAT ≈ HitTimeL1 + MissRateL1 * MissPenaltyL1
L2 reduces L1 miss penalty – saves access to memory
Now, on L1 miss we access L2, but not memory
  MissPenaltyL1 ≈ HitTimeL2 + MissRateL2 * MissPenaltyL2
L2 Cache is larger (better HitRate), but has higher latency
Example:

## Slide 9: Prefetching
Prefetching – predict future memory accesses
Instruction Prefetching
  On a cache miss, prefetch sequential cache line
Data Prefetching
  Next sequential: on a cache miss, prefetch sequential cache line
  Stride: remember the repetitive step of a load and prefetch data in advance
  General direction: even if there is no fixed stride can understand general direction and prefetch along it
Software Prefetching: special prefetching instructions
Prefetch Limitations
  Prefetching relies on extra memory bandwidth
  Too aggressive / inaccurate prefetching slows down demand fetches

## Slide 10: Code Optimization: Merging Arrays
Merge arrays into an array of compound elements
  Before: two sequential arrays
int val[SIZE];
int key[SIZE];
  After: One array of structures
struct merge {
int val;
int key;
} merged_array[SIZE];
Reduce conflicts between val and key
Improves spatial locality

## Slide 11: Code Optimization: Loop Fusion
Combine loops that have same looping and work with the same memory
  Assume each element is 8 bytes, 32KB cache, 64 B/line
  for (i = 0; i < 10240; i++)
  a[i] = 1 / a[i];
  …
  for (i = 0; i < 10240; i++)
  sum = sum + a[i];
  Fuse the loops
  for (i = 0; i < 10240; i++) {
  a[i] = 1 / a[i];
  sum = sum + a[i];
  }
Improves temporal locality

## Slide 12: Code Optimization: Loop Interchange
Change loops nesting to access data in order stored in memory
  Two dimensional array in memory:
x[0][0] x[0][1] … x[0][99] x[1][0] x[1][1] …
  Before:
  for (j = 0; j < 100; j++)
  for (i = 0; i < 5000; i++)
  x[i][j] = 2 * x[i][j];
  Improves spatial locality
  Sequential accesses instead of striding through memory every 100 words
  for (j = 0; j < 100; j++)
  After:
  for (i = 0; i < 5000; i++)
x[i][j] = 2 * x[i][j];
  for (i = 0; i < 5000; i++)
  for (j = 0; j < 100; j++)
  x[i][j] = 2 * x[i][j];

## Slide 13: Memory Coherence in Multi-Core/Processor System
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
Example:
Memory system must be coherent
  Cores should see memory identically
  Cores should see the latest state of memory
[X] ≡ 10
[X] ≡ 20
20
Memory: Mem[X] ≡ 10
Core 0: a = Mem[X] # a = 10
Core 1: Mem[X] = 20
Core 0: b = Mem[X] # b = 10
miss
miss
[X] ≡ 10
hit
Error: read the old value from the local cache
Problem: one core modifies data that another core has in its local cache
[X] ≡ 10
20

## Slide 14: Coherence protocol: MESI
Coherency protocols describe how to handle writes and reads in a multi-core system in order to maintain memory coherence
The most famous one is MESI
  Define the four possible state of a cache line
  Describe transactions from one state to another (next foils)
 | Is the line valid? | Do others have this line? | Has it been modified?
Invalid | NO | NA | NA
Shared | YES | YES | NO
Exclusive | YES | NO | NO
Modified | YES | NO | YES
There is no state when a line is modified and contained by multiple cores

## Slide 15: MESI Operating Example
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
[X] ≡ 25
[X] ≡ 35
[X] ≡ 25
[X] ≡ 25
Memory: Mem[X] ≡ 25
Core 0: a = Mem[X] # a = 25
Core 0: Mem[X] ≡ 35
Core 1: b = Mem[X] # b = 35
  Snoop [X]
    Core 0 writeback [X]
Core 1: Mem[X] ≡ 45
  Request ownership for [X]
    Core 0 invalidate [X]
35
[X] ≡ 25
(1, 0)
E
M
35
35
[X]
(1, 1)
S
S
[X]
I
(0, 1)
[X]
M
45

## Slide 16: MESI State Diagram
R – read
W – write
S – line shared
!S – line not shared
SN – snoop
RO – request ownership
I
E
M
S
R or SN
R or W
R
SN or RO
W
SN
RO
R and !S
RO
R and S
SN
RO
W
W

## Slide 17: The End