## Slide 1: Out-Of-Order Execution (part I)
Alexander Titov
14 March 2015

## Slide 2: Superscalar: wide pipeline
Pipeline exploits instruction level parallelism (ILP)
Can we do it better?
  Need to double HW structures
  Max speedup is 2 instruction per cycle (IPC = 2)
  The real speedup is less due to dependencies and in-order execution
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
F | Stall
– Yes, execute instructions in parallel

## Slide 3: Is Superscalar Good Enough?
Theoretically can execute multiple instructions in parallel
  Wider pipeline → more performance
But…
  Only independent subsequent instructions can be executed in parallel
  Whereas subsequent instructions are often dependent
  So the utilization of the second pipe is often low
Solution: out-of-order execution
  Execute instructions based on the “data flow” graph, (rather than program order)
  Still need to keep the visibility of in-order execution

## Slide 4: Data Flow Execution
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
In-order execution
Out-of-order execution
1
3
4
2
5
6
r1
r5
r6
r4
r8
Example:
Data Flow Graph
1
3
4
2
6
5
3
4
6
5
1
2

## Slide 5: Can SW Help?
Parallel algorithms
Sequential hardware
Sequential code (ISA)
The algorithms are parallel and SW sees that parallelism
Initially, HW was very simple: sequential execution, one instruction at a time
There were no need to represent parallelism to HW
Sequential code representation seemed natural and convenient

## Slide 6: Can SW Help?
Sequential hardware
Then, technology allowed building wide and parallel HW, but the code representation had stayed sequential
Decision: extract parallelism back by means of HW only
Due to compatibility still need look like sequential HW
Parallel algorithms
Sequential code (ISA)
Sophisticated
parallel
hardware
Visibility of
sequential HW

## Slide 7: Why Is Order Important?
Many mechanisms rely on original program order and unambiguous architectural state
  Precise exceptions: nothing after instruction caused an exception can be executed
(1) r3  r1 + r2
  (2) r5  r4 / r3
(3) r2  r7 + r6
  Interrupts: need to save the arch state to be able to correctly restart the program lately
(1) r5  Mem[r4]
(2) r3  r1 + r2
(3) r2  r7 + r6
  And others…
  Instructions were executed in the following order: (1) → (3) → (2). Then, (2) led to exception.
  For example, (2) and (3) were executed, but (1) was not. Then, interrupt occurred. From what IP to restart? What to save?
  Where to take old value or r2?
  From what IP to restart? What to save?

## Slide 8: Maintaining Arch State
Solution: support two state, speculative and architectural
Update arch state in program order using special buffer called ROB (reorder buffer) or instruction window
  Instructions written and stored in-order
  Instruction leaves ROB (retired) and update arch state only if it is the oldest one and has been executed
Retirement
Instruction window
Out-of-order execution
Fetch & Decode
Sequential code
Visibility of
sequential execution
Out-of-order
In-order
Legend:
Speculative state
Architectural state

## Slide 9: Dependency Checking
For each source check readiness of its producer
Fetch
Retire
HW instruction window (ROB)
Ready, but not executed
Executes
Legend:
Not ready
?
r3  r1 + r2
r1  …
4
7
1
3
0
5
6
2
8
10
9
11
12
13
14
15
…  r3 + …
r2  …
ready
not ready
.., #15
Src1:
Src2:
Consumers:
  If both sources are ready then instruction is ready
  If a source is not ready, write the instr# into the consumer list of producer
When instruction becomes ready, it says its consumers that their sources become ready too
Is it enough?
No, need to wait until the previous value of the destination is read by all consumers.
Is it a real dependency?
r3
It a false dependency.

## Slide 10: How Large Is Window Needed?
In short, the larger window → the better
  Find more independent instructions
  Hide longer latencies (e.g., cache misses, long operations)
Example
  The modern CPU has a window of 200 instructions
  If we want execute 4 instruction per cycle, then we can hide latency of 50 cycles
  It is enough to hide L1 and L2 misses, but not L3 miss (≈200 cycles)
But, there are limitations to find independent instructions in a large window:
  branches and false dependencies

## Slide 11: Limitation: Branches
How to fill a large window from a single sequential instruction stream in presence of branches?
Fetch
Retire
Branch with unknown condition
All subsequent instructions are fetch according to prediction
…
Speculatively fetched instructions can be executed too
Verify the branch prediction
If prediction was wrong, all the subsequent instructions are deleted
deleted
How harmful branches are?
  In average, each 5th instruction is a branch
  Assume accuracy of prediction is 90% (looks high, isn’t it?)
  The probability that 100th instruction in the window will not be removed is (90%)^20 = 12%
Accuracy of branch prediction is very important for Out‑Of‑Order Execution
→ Using branch prediction!
  (e.g., (99%)^20 = 82%)

## Slide 12: Limitation: False Dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
Out-of-order execution
Example:
1
3
4
2
5
6
r1
r5
r6
r4
r8
Data Flow Graph
4
3
6
5
1
2
r1
r1
r1
False Dependencies:
Write-After-Write: (1) → (3)
Write-After-Read: (2) → (3)
Significantly decrease performance

## Slide 13: Eliminating False Dependencies
(2) …  ar3 + …
(1) ar3  …
(4) …  ar3 + …
(3) ar3  …
Register name is similar to variable name in a program
  It is just a label to identify dependency among operations
Difference: number of register names is limited by ISA
  It is one of the main reason of false dependencies
HW can contain more registers in the speculative state (i.e. more names) than ISA and perform dynamic register renaming
  Number of registers in arch state is not changed (= ISA)
Requirements
  Producer and all its consumers art renamed to the same speculative register
  Producer writes to the original arch register at retirement
sr10
sr10
sr11
sr11

## Slide 14: Register Renaming Algorithm
Redo register allocation that was done by compiler
Eliminate all false dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r1  r5 + 1
(4) r6  r6 – r3
(5) r4  load [ r1 + r6 ]
(6) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15

## Slide 15: End of Part I