## Slide 1: Out-Of-Order Execution (part II)
Alexander Titov
4 April 2015

## Slide 2: Refresher: OOO Exe
Superscalar – wide pipeline (4-5 in modern CPU)
Out-of-order – execute according real dependencies (“data flow”) rather than program order
Advantages:
  Exploit parallelism beyond adjacent instructions
  Hide long latencies (e.g., cache misses)
Compatibility: need to maintain visibility of in-order execution
  Precise exceptions, memory model, etc.

## Slide 3: Refresher: HW Instruction Window
Two states are supported: speculative and architectural
Instruction window (ROB) keeps all in-flight instructions and allows reconstruction of the original order at retirement
The large window the better performance
Limitations:
  False dependencies -> rename registers
  Branches -> accurate dynamic prediction
  Complex HW (so far we did not talk about that)

## Slide 4: Why Is ROB Complex?
The two complex searches though all ROB entries
  At allocation (once per each instruction): to identify producers of the instruction sources
  At scheduling (every cycle): to identify ready instructions and send them to execution
The larger ROB the longer search and large HW structures
  Prevents from doing ROB really large -> loose potential performance
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 5: Scheduler Queue
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 6: Scheduler Queue
Out-of-order execution
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
  All checks (allocation and scheduling) are performed on it
  Use RON only for order reconstruction at retirement
PRF
EXE
Scheduler
Memory
ROB
SQ
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Write data
from decoder

## Slide 7: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
1
5
3
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At allocation of (3):
Search for Src1 producer
  Found in entry 1
    Mark dependency
Search for Src2 producer
  Found in entry 5
    Mark dependency
At least one is found -> not ready
false

## Slide 8: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At completion of (1,2):
Reset dependency to all consumers
For each entry check its readiness
false
true

## Slide 9: Memory Dependencies
OOO Scheduler can track dependency through registers, but not through memory
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Unlike register dependencies, memory dependency cannot be known at allocation
    (1) Mem[r2]  …
    …
    (6) …  Mem[r3]
Decision: load should wait until all the previous stores write into the memory (cache)
It works, but it is too slow (stores write after retirement)
  If instruction(6) will executes before (1) lit will read a wrong value from memory
  Registers r2 and r3 can have the same values

## Slide 10: Store Forwarding
Faster decision: load waits only if there is some older store with not calculated address
If addresses of all the previous stores are known and there is not intersection with them, then load can be executed
In case of intersection, the load is waiting until the data of the store is ready and take it directly from the store

## Slide 11: End of Part I