## Slide 1: Digital Combinational Circuits
Titov Alexander
11/27/2013

## Slide 2: Layers of Abstraction in Computes Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture
Less about physics, wires and transistors…
More about logical circuits

## Slide 3: Physical Abstraction
Real physical circuits deal with physical properties, such as voltages and currents
Digital circuits use the abstractions of 0 and 1 to represent the presence or absence of these physical properties (signals) rather than a continuous range
Logic 1
Logic 0
Weak 1
Weak 0
undefined
5 V
3.5 V
1.5 V
0 V
voltage
It could not be a stable state: should not occur in the circuit except during transitions from one state to he other

## Slide 4: Boolean Algebra
Boolean Algebra (BA) works with object that can take only two values (true and false, or 1 and 0).
    Such object is called a Boolean object (term bit of information is used in CS)
    BA defines operations on Boolean objects → Boolean operations and functions
    It is convenient to represent these operations and functions via truth tables:
a | b | c
c = F(a,b)
b
a
c
Boolean function
Truth table
a | b | c
0 | 0 | 
a | b | c
0 | 0 | 
a | b | c
0 | 0 | 
a | b | c
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
a | b | c
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 5: Main Boolean operations
The simplest Boolean operation is …
AND (or Boolean multiplication)
inversion (NOT)
x
!x
x | x
0 | 1
1 | 0
x*y
x
y
x | y | x*y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
0
1

## Slide 6: Main Boolean operations
OR (or Boolean addition)
x+y
x
y
x | y | x+y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
1
XOR (or exclusive OR, or addition by module 1)
x | y | x  y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0
x + y
x
y
= x*!y + !x*y

## Slide 7: Main axioms
There about ten axioms that can be used to create new or to simplify existed functions
Axiom | AND form | OR form
Identity law | 1*x = x | 0 + x = x
Idempotent law | x*x = x | x + x = x
Inverse law | !x*x = 0 | !x + x = 1
Commutative law | x*y = y*x | x + y = y + x
Associative law | (x*y)*z = x*(y*z) | (x + y) + z = x + (y + z)
Distributive law | x*y + z = (x + z)(y + z) | (x + y)*z = x*z + y*z
De Morgan's laws | !(xy) = !x + !y | !(x + y) = !x * !y
… |  | 
There are a lot of other useful equations:
n(n(x) + y) + n(n(x) + n(y)) = x
(Huntington equation)

## Slide 8: Boolean functions
Boolean operations can be combined into functions
F(x, y, z) = x + !y*z
x
y
z
x + !y*z
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | … | … | 1
0
1
0
0

## Slide 9: Examples of reduction
F = (!x * !y * !z) + (!x * y * z) + (x * !y * !z) + (x * y * !z) =
= (!x * !y * !z) + (!x * y * z) + (x * !z) * (!y + y) =
= (!x * !y * !z) + (!x * y * z) + (x * !z) =
= !x * (!y * !z + y * z) + (x * !z) =
= !x * (!y  z) + (x * !z).
= (!x + x) * (!y * !z) + (!x * y * z) + (x * y * !z) =
= (!y * !z) + y * (!x * z + x * !x) =
= (!y * !z) + y * (x  z) =
= !(y + z) + y * (x  z).

## Slide 10: Canonical disjunctive normal form (CDNF)
CDNF is an algorithm of reconstructing a Boolean function from its truth table
    Take lines with ‘1’ only
    Conjunct all variables in line with correct sign
    Make disjunction on expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
!x * !y * !z
!x * y * z
x * !y * !z
x * y * !z
F = (!x * !y * !z) + (!x * y * z) + (x * !y * !z) + (x * y * !z)

## Slide 11: Canonical conjunctive normal form (CCNF)
CCNF is an algorithm of reconstructing a Boolean function from its truth table
    Take lines with ‘0’ only
    Make disjunction on all variables in line with correct sign
    Conjunct expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
x + y + !z
x + !y + z
!x + y + !z
!x + !y + !z
F = (x + y + !z)(x + !y + z)(!x + y + !z)(!x + !y + !z)

## Slide 12: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational :
Qt = F(xt, yt, zt, …)
Combinational circuit (scheme) is an implementation of a combinational function
A lot of things can be implemented using combinational circuits
    Just a few examples that will be presented soon: summator, decoder, multiplexer

## Slide 13: Half adder scheme
half +
y
x
sum
carry
x | y | s | c
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0
1
1
0
0
0
0
1
It is an adder, but it is not a full adder, because it does not have input carry
Calculations:
It is an adder, but it is not a full adder, because it does not have input carry
Sum =
= !x * y + x * !y =
= x  y
Carry = x * y
x
y
s
c

## Slide 14: Full adder scheme
half +
yn
xn
cn-1
half +
sn
Cn
0 | 0 | 1 |  | 
0 | 1 | 1 |  | 
1 | 0 | 1 |  | 
1 | 1 | 1 |  | 
1
0
0
1
0
1
1
1
It is called a full adder
+
y
x
sum
carry
c
xn | yn | cn-1 | sn | cn
0 | 0 | 0 |  | 
0 | 1 | 0 |  | 
1 | 0 | 0 |  | 
1 | 1 | 0 |  | 
0
1
1
0
0
0
0
1

## Slide 15: Wide adder
+
yn
xn
+
yn+1
xn+1
cn-1
cn
cn+1
sn
sn+1

## Slide 16: Multiplexer

## Slide 17: Arithmetic Logic Unit

## Slide 18: Thank You