## Slide 1: Boolean Algebra and Combinational Circuits
Alexander Titov

## Slide 2: Topics of The Lecture
Boolean Algebra
  math apparatus for Digital Circuits
Combinational Circuits
  Circuits without memory: their output is defined by the given input only
  Examples: all arithmetic (adder, multiplier, etc.), decoder, multiplexer and much more
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Fig.: Position in the layers of abstraction

## Slide 3: Digital Abstraction
Logic 1
Logic 0
To design an electrical circuit we need to deal with real physical properties
In the abstraction of Digital circuits we reduce all physical properties to 0 and 1 states
It cannot be a stable state: should not occur in the circuit except during transitions from one state to the other
Logic 1
Weak 1
Weak 0
1.2
1.0
0.2
voltage
Logic 0
0.0
undefined
Supply voltage
Ground
Fig.: Maxwell’s equations
→ complicated for large systems
X

## Slide 4: Boolean Algebra
Boolean Algebra works with objects that can have only two states (true and false, or 1 and 0)
  Such object is called a Boolean object (term bit of information is used in CS)
  Boolean Algebra defines operations on Boolean objects → Boolean operations and functions
  It is convenient to represent these operations and functions via truth tables:
George Boole
(1815 – 1864)
English mathematician, philosopher and logician
c = F(a,b)
b
a
c
Fig.: Boolean function
Fig.: Truth table
a | b | c
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
a | b | c
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 5: Main Operations
The simplest Boolean operation is …
x
!x
x | !x
0 | 1
1 | 0
AND (or Boolean multiplication)
inversion (NOT)
x*y
x
y
x | y | x*y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
0
1

## Slide 6: Main Operations (2)
OR (Boolean addition)
XOR (exclusive OR, addition by module 1)
x+y
x
y
x | y | x+y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
1
x + y = !x*y + x*!y
x
y
x | y | x  y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0

## Slide 7: Boolean Functions
Boolean operation can be combined into functions
F(x, y, z) = x + !y*z
x
y
z
x + !y*z
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | … | … | …
0
1
0
0

## Slide 8: Main axioms/laws
De Morgan's laws | !(xy) = !x + !y | !(x + y) = !x * !y
Distributive law | x*y + z = (x + z)(y + z) | (x + y)*z = x*z + y*z
Associative law | (x*y)*z = x*(y*z) | (x + y) + z = x + (y + z)
Commutative law | x*y = y*x | x + y = y + x
Inverse law | !x*x = 0 | !x + x = 1
Idempotent law | x*x = x | x + x = x
Identity law | 1*x = x | 0 + x = x
Axiom | AND form | OR form
Null law | 0*x = 0 | 1 + x = 1

## Slide 9: Main axioms/laws
Identity law | 1*x = x | 0 + x = x
Axiom | AND form | OR form
Null law | 0*x = 0 | 1 + x = 1
x | y | x*y
0 (closed) | y | 0
1 (open) | y | y
x | y | x*y
0 (open) | y | y
1 (closed) | y | 1
AND and OR can be used as a logical key
Useful to reconstruct a function from the given truth table

## Slide 10: Canonical disjunctive normal form (CNDF)
CDNF is an algorithm of reconstructing a function from its truth table
  Take lines with ‘1’ only
  Conjunct all variables in line with correct sign
  Make disjunction on expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
!x !y !z
!x y z
x !y !z
x y !z
F = (!x !y !z) + (!x y z) + (x !y !z) + (x y !z)

## Slide 11: Canonical conjunctive normal form (CCDF)
CCNF is an algorithm of reconstructing a function from its truth table
  Take lines with ‘0’ only
  Make disjunction of all variables in line with correct sign
  Make conjunction of the expressions
x | y | z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
x + y + !z
x + !y + z
!x + y + !z
!x + !y + !z
F = (x + y + !z)(x + !y + z)(!x + y + !z)(!x + !y + !z)

## Slide 12: Karnaugh Map
The topic was presented on the whiteboard

## Slide 13: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational:
Q = F(x, y, z, …)
Combinational circuit (scheme) is an implementation of a combinational function
Such circuit does not depend on its previous output
  Has no state
  Cannot remember data

## Slide 14: Comparator
Two binary numbers are equal if their bits are equal
Comparator returns true if numbers are equal
x0 | x1 | y0 | y1 | Q
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
… | … | … | … | 0
Q = (!x0 !x1 !y0 !y1) + (x0 !x1 y0 !y1) + (!x0 x1 !y0 y1) +
(x0 x1 y0 y1)
= !(x0  y0) * !(x1  y1)
x | y | !(x  y)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Fig.: XNOR truth table
x0
y0
x1
y1
Q
Fig.: 2-bit digits comparator truth table

## Slide 15: Multiplexor
Multiplexor (mux) transfers one of the data input to output according to the control input
x
y
Q
c
x | y | c | Q
1 | 0 | 0 | 1
0 | 1 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
… | … | … | 0
Q = x !y !c + !x y c + x y !c + x y c
Q = x !c (!y + y) + y c (!x + x)
Q = x !c + y c
y
c
x
c
Q

## Slide 16: 4-input Multiplexor
A0 | A1 | Out
0 | 0 | M0
0 | 1 | M1
1 | 0 | M2
1 | 1 | M3
A0
A1
d0
d1
d2
d3
M0
M1
M2
M3
A0 | A1 | d0 | d1 | d2 | d3
0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Truth table of the Decoder
Truth table of the Multiplexer

## Slide 17: Half Adder
It is an half adder, because it does not have input carry
half +
y
x
sum
carry
x | y | s | c
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0
1
1
0
0
0
0
1
Calculations:
Sum = !x * y + x * !y =
= x  y
Carry = x * y
x
y
s
c

## Slide 18: Full Adder
half +
yn
xn
cn-1
half +
sn
Cn
+
y
x
sum
carry
c
+
yn
xn
+
yn+1
xn+1
cn-1
cn
cn+1
sn
sn+1

## Slide 19: Questions?