## Slide 1: Integrated Circuits Implementation: CMOS
Alexander Titov

## Slide 2: Topics of The Lecture
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Fig.: Position in the layers of abstraction

## Slide 3: Why Transistor (MOSFET)?
Transistors are the fundamental building blocks for all digital circuits
The main advantage of transistors over other devises (i.e., vacuum tubes) is that they are:
  very small (< 16nm)
  reliable (the 1946 ENIAC, with over 17,000 vacuum tubes, had a tube failure on average every two days)
  power efficient (almost don’t consume energy when the state is not changed)
  cheep (production cost of a processor is about several dollars, but it contains billions of transistors)

## Slide 4: MOSFET
The metal-oxide-semiconductor field-effect transistor (MOSFET) acts as a voltage-controlled switch with three terminals: source, drain, and gate
  The gate controls whether current can pass from source to drain or not
There are two variations of the MOSFET: the n-channel (this slide) and the p-channel
Source
Gate
Drain
+
-
-
-
+
+
+
-
-
-
Metal
Oxide layer
P-type semiconductor
N-type semiconductor
Gate
Drain
Source

## Slide 5: Diffusion process
Holes and electrons diffuse into the n-type and p-type semiconductors correspondently
The diffusion process creates the balancing field (Ed) that prevents deeper diffusion → no current in stable state
Source
Gate
Drain
+
+
+
+
-
-
-
-
-
-
Ed
Ed
Ed
+
+
+
+
-
-
-
-
-
-
Ed
Ed
Ed

## Slide 6: Closed State for N-type MOSFET
For N-type MOSFET if the gate is not connected (high-impedance state, Z) or equal to 0 there is not current between source and drain
  More precisely when Vgs < Vt, where Vt is the threshold voltage needed to create a channel
One of n-p junction is always closed
Source
Gate
Drain
0/Z
0
Z
Ecc
Ed
This p-n junction is closed: its field balances the field of the supply
No current through this p-n junction
Vcc
Vg
Vd
Vs
Vgs < Vt

## Slide 7: Open State for N-type MOSFET
For N-type MOSFET if the gate is equal to 1 then the transistor is open: the source value pass to the drain
  More precisely when Vgs > Vt
The current passes though the small N-type channel created by the gate field
Source
Gate
Drain
+
+
+
+
-
-
1
0
0
N-type channel with free conductors (electrons)
Eg
Vcc
Vg
Vgs > Vt
Vd
Vs
Rc

## Slide 8: N-Type Truth Table
N-Type is not suitable to transfer 1 well
Gate | State | Input (Source) | Output (Drain)
0 | Off (not conduct) | any | Z
1 | On (conduct) | 0 | 0
 |  | 1 | weak 1
Vd
= Vcc - Vt
Vs = 1 = Vcc
Vg = 1 = Vcc
Vd = ?
Rc
Vs = 1 = Vcc
Vg = 1 = Vcc
Open only if Vgd > Vt
Vs0 = 1 = Vcc
Vs1 = 1 = Vcc
Vg0 = 1 = Vcc
Vd0
= Vcc - Vt
Vd1
= Vcc – 2*Vt
Gate | State | Input (Source) | Output (Drain)
0 | Off (not conduct) | any | Z
?

## Slide 9: N and P-type MOSFET
P-type MOSFET (similar to N-type, but all is inverted):
Gate
Drain
Source
Gate | State | Input (Source) | Output (Drain)
0 | Off (not conduct) | any | Z
1 | On (conduct) | 0 | 0
 |  | 1 | weak 1
Gate | State | Input (Source) | Output (Drain)
1 | Off (not conduct) | any | Z
0 | On (conduct) | 1 | 1
 |  | 0 | weak 0
Gate
Drain
Source
N-type MOSFET

## Slide 10: CMOS Circuits
Complementary metal–oxide–semiconductor (CMOS) is a technology for constructing integrated circuits
The main characteristics of CMOS devices is low static power consumption
  There is no current in a static state (i.e. the power supply is never connected to the ground in a static state)
  … except small leakage currents
CMOS schemes always contain two complementary parts
  One part consists of P-type transistors and is connected to the power supply and provides 1 to the output
  The other consists of N-type transistors and is connected to the ground and provides 0 to output
  When one part is turned on the other part is disabled (provides Z)

## Slide 11: CMOS Inverter
Input | Output
0 | 1
1 | 0
Gate
Drain
Source
Gate
Drain
Source
0
Vcc
1
Input | Output
0 | Z
1 | 0
Input | Output
0 | 1
1 | Z
0
Vcc
1
Input
Output
1
0
Z
The bottom part
The top part
The full scheme

## Slide 12: CMOS NAND Circuits
A | B | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0
A
B
Output
Vcc
1
A
Output
B
Vcc
1
A
Output
B
0
A
B
The bottom part
The top part
The full scheme

## Slide 13: Questions?