## Slide 1: Sequential Circuits
Alexander Titov

## Slide 2: Topics of The Lecture
Register-Transfer Level (RTL)
Gates
Devices (Transistors)
Circuits
Physics
Fig.: Position in the layers of abstraction

## Slide 3: Refresher: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational:
Combinational circuit (scheme) is an implementation of a combinational function
A lot of things can be implemented using combinational circuits
  We already know: comparator, multiplexer, adder
  We will see more in the next lectures
But, combinational circuits have a significant limitation:
Qt = F(xt, yt, zt, …)
they cannot remember any information

## Slide 4: Combinational vs. Sequential
Button pressed
Button released
time
off
on
on
on
off
off
off
on
off
off
Combinational
Sequential
lamp
Strongly depends on input!
“Remember” that button was pressed
button
Event “button pressed”

## Slide 5: Sequential Circuits 10,000 foot view
Combinational Logic
Memory Device
Store the current state of the circuit
Next state
Current state
Input
Output
Synchronization
allows to update the state

## Slide 6: Sequential Functions
If the output of a function depends not only on the current input, but on the previous ones, then the function is called sequential
Sequential circuit is an implementation of a sequential function
Their main advantage is ability to remember the previous state
  Any circuit with memory is a sequential circuits
Qt = Q(xt, yt, zt, …, St)
S(xt-1, yt-1, zt-1, …, St-1))
S(xt-2, yt-2, zt-2, …, St-3)))

## Slide 7: SR Latch
S | R | Qt-1 | Qt
x | y | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Q
!Q
x
y
out
y
out
≡
x
y
out
0
≡
out
Q
!Q
reset
set
0
0
1
0
1
1
0
1
NOR:
SR flip-flop truth table:
The simplest store element:
SR flip-flop scheme:
0
1
0
0
Q
Q
0
1
Q
0
1
0
Q
1
1
1
Q
0
reset
set
Q
!Q
Prohibited state
0
1
How to write into it?

## Slide 8: SR Latch Timing Diagram
reset
set
Q
!Q
R
!Q
S
Q
S | R | Qt-1 | Qt
0 | 0 | Q | Q
0 | 1 | Q | 0
1 | 0 | Q | 1
1 | 1 | Q | 0
S
0
1
R
0
1
Q
0
1
!Q
0
1
?
?
… but, which one is faster?
It depends on many factors (e.g., layout, temperature)
The output will be determined by the fastest signal

## Slide 9: D Latch
Don’t have prohibited states
Asserted by a level of the write enable signal (we) ← Synchronization
Store one bit of information
Can be used as memory cell in static memory arrays
S
Q
R
!Q
Write enable
Data
D | we | Qt-1 | Qt
D | 0 | Q | Q
0 | 1 | Q | 0
1 | 1 | Q | 1
D
we
Q

## Slide 10: D Flip-Flop
Unlike a latch, a flip-flop is open for write only at switching of the write enable signal (from 0 to 1, or from 1 to 0, or both)
More expense (2 D-latches), but extremely helpful in building a CPU pipeline
D
we
Q
D
we
Q
D
we
Q
D | we | Qt-1 | Qt
D | 0 | Q | Q
D | 1 | Q | Q
D | 1→0 | Q | Q
D | 0→1 | Q | D

## Slide 11: Memory Arrays
in
out
e
in
out
e
in
out
e
in
out
e
demultiplexor
multiplexor
in
out
Memory
Array
address
input data
output data
2
1
1
Write enable
address
address

## Slide 12: Single port 4x1 Memory Array
Multiplexer
Decoder
Write control
s0 | s1 | d0 | d1 | d2 | d3
0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Truth table of the Decoder
1
0
0
1
0
0
0
0
0
0
0
0
0
0
Q
Q
Q

## Slide 13: Single port 4x2 Memory Array
Multiplexer bit[0]
Decoder
Write control
Multiplexer bit[1]

## Slide 14: Questions?